## Slide 2: CPUs and GPUs have fundamentally different design philosophies
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 9: Nvidia Kepler
192 Floating Point processing units per streaming multiprocessor
256KB Level 2 Cache
Introduction of dynamic parallelism scheduler
Multiple kernel execution with scheduling

## Slide 11: Nvidia Maxwell
128 Floating Point processing units per streaming multiprocessor
2MB Level 2 Cache
Massive Power Usage Reduction
Native shared memory atomic operations and CAS
Isolated Warp Scheduling

## Slide 12: NVIDA TX2 Configuration

## Slide 13: NVIDIA PASCAL GP100

## Slide 20
OpenMP
An accepted standard developed in the late 1990s by a group of industry specialists.
Consists of a small set of compiler directives, augmented with a small set of library routines and environment variables using the base language Fortran and C/C++.
The compiler directives can specify such things as the par and forall operations described previously.

## Slide 21
Parallel Regions
Fork-Join Parallelism but thread based:
Master thread spawns a team of threads as needed
Parallelism can be added incrementally
  sequential program evolves into a parallel program
Master Thread

## Slide 33: Jacobi Iteration 2D C++ Code

## Slide 34: Jacobi Iteration 2D C++ Code

## Slide 36: 2D Jacobi Iteration – Identify Parallelism

## Slide 37: 2D Jacobi Iteration – Identify Parallelism

## Slide 39: 2D Jacobi Iteration – Express Parallelism

## Slide 40: 2D Jacobi Iteration – Express Parallelism OpenMP Solution

## Slide 42: OpenACC Parallel Directive
Starts parallel execution on accelerator
Specified by:
  #pragma acc parallel [clause [,clause]…] new-line
structured block
When encountered:
  Gangs of workers threads are created to execute on accelerator
  One worker in each gang begins executing the code following the structured block
  Number of gangs/workers remains constant in parallel region

## Slide 43: OpenACC Parallel Directive
The clauses for the #pragma acc parallel directive are:
  if( condition)
  async [(scalar-integer-expression)]
  num_gangs (scalar-integer-expression)
  num_workers (scalar-integer-expression)
  vector_length (scalar-integer-expression)
  reduction (operator:list)
  copy (list)
  copyout (list)
  create (list)
  private (list)
  firstprivate (list)

## Slide 44: OpenACC Loop Directive
Used to describe what type of parallelism to use to execute the loop in the accelerator.
Can be used to declare loop-private variables, arrays and reduction operations.
Specified by:
  #pragma acc loop [clause [,clause]…] new-line
    for loop

## Slide 45: OpenACC Loop directive clauses
collapse clause
  Specifies how many tightly nested loops are associated with the loop construct.
seq clause
  Specifies that a loop needs to be executed sequentially by the accelerator.
independent clause
  Specifies that there are no data dependences in the loop.
private clause
  Specifies that a copy of each item on the list will be created for each iterations of the loop.
reduction clause
  Specifies that a reduction need to be perform associated to a gang, worker or vector.
tile clause
  Breaks the next 1 or more loops into tiles based upon the specified dimensions.

## Slide 46: 2D Jacobi Iteration – Express Parallelism OpenMP Solution

## Slide 47: 2D Jacobi Iteration – Express Parallelism OpenACC Solution

## Slide 48: 2D Jacobi Iteration – Express Parallelism OpenACC Solution – common parallel section

## Slide 49: 2D Jacobi Iteration – Express Parallelism OpenACC Solution – more expressive solution

## Slide 50: 2D Jacobi Iteration – Express Parallelism OpenACC Solution – common parallel section

## Slide 51: Building the Code
pgc++ laplace2d_acc.cpp -o laplace2d_acc -acc -ta=nvidia -Minfo=accel -lm -fast
main:
72, Accelerator kernel generated
Generating Tesla code
74, #pragma acc loop gang /* blockIdx.x */
Generating reduction(max:error)
76, #pragma acc loop vector(128) /* threadIdx.x */
83, #pragma acc loop gang /* blockIdx.x */
85, #pragma acc loop vector(128) /* threadIdx.x */
72, Generating implicit copyin(A[:][:])
Generating implicit copyout(A[1:4094][1:4094])
Generating implicit copy(error)
Generating implicit copyout(Anew[1:4094][1:4094])
76, Loop is parallelizable
85, Loop is parallelizable

## Slide 52: 2D Laplace Measured Speedup OpenMP and OpenACC

## Slide 54: 2D Jacobi Iteration – Excessive Data Transfer

## Slide 58: 2D Jacobi Iteration – Express Parallelism OpenACC Solution – more expressive solution

## Slide 60: 2D Jacobi Iteration – Express Parallelism OpenACC Solution – common parallel section

## Slide 61: Building the Code
pgc++ laplace2d_acc.cpp -o laplace2d_acc -acc -ta=nvidia -Minfo=accel -lm -fast
main:
69, Generating copy(A[:][:])
Generating create(Anew[:][:])
73, Accelerator kernel generated
Generating Tesla code
75, #pragma acc loop gang /* blockIdx.x */
Generating reduction(max:error)
77, #pragma acc loop vector(128) /* threadIdx.x */
84, #pragma acc loop gang /* blockIdx.x */
86, #pragma acc loop vector(128) /* threadIdx.x */
73, Generating implicit copy(error)
77, Loop is parallelizable
86, Loop is parallelizable

## Slide 62: 2D Laplace Measured Speedup OpenMP and OpenACC

## Slide 64: 2D-Laplace Shaping Example
Also assume that the anew and a arrays are allocated dynamically
anew = new double[NN*NM]; a = new double[NN*NM];

## Slide 65: 2D-Laplace Shaping Example

## Slide 73: OpenACC Kernels Directive
Defines a region of a program that is to be compiled into a sequence of kernels for execution on the accelerator
  Each loop nest will be a different kernel
  Kernels launched in order in device
  Specified by:
#pragma acc kernels [clause [,clause]…] new-line
structured block

## Slide 74: OpenACC Kernels Directive Clauses
Kernels directive may not contain nested parallel or kernel directives.
The clauses for the !$acc kernels directive are:
  copy (list)
  copyin (list)
  copyout (list)
  create (list)
  private (list)
  firstprivate (list)
  if( condition)
  async [(scalar-integer-expression)]

## Slide 76: OpenACC Kernels Directive Clauses
if clause
  Optional clause to decide if code should be executed on accelerator or host
async clause
  Specifies that a parallel accelerator or kernels regions should be executed asynchronously
  The host will evaluate the integer expression of the async clause to test or wait for completion with the wait directive

## Slide 77: OpenACC Kernels Directive Clauses
The clauses for the #pragma acc kernels directive are:
  present (list)
  present_or_copy (list)
  present_or_copyin (list)
  present_or_copyout (list)
  present_or_create (list)
  deviceprt (list)
  num_gangs
  num_workers
  vector_length

## Slide 78: OpenACC Kernels Directive Clauses
present clause
  Specifies items are already present in the accelerator memory
  The items were already allocated on other data, parallel or kernel regions. (i.e. inter-procedural calls)
present_or_copy clause
  Tests if a data item is already present in the accelerator. If not, it will allocate the item in the accelerator and copy-in and out its value from/to the host
present_or_copyin clause
  Test if a data item is already present in the accelerator. If not, it will allocate the item in the accelerator and copy-in its value from the host

## Slide 79: OpenACC Kernels Directive Clauses
present_or_copyout clause
  Test if a data item is already present in the accelerator. If not, it will allocate the item in the accelerator and copy-out its value to the host
present_or_create clause
  Test if a data item is already present in the accelerator. If not, it will allocate the item in the accelerator (no initialization)
  anew = new double[NN*NM]; a = new double[NN*NM];

## Slide 80: OpenACC Update Directive
Used within a data region to update / synchronize the values of the arrays on both the host or accelerator
Specified by:
  #pragma acc update [clause [,clause]…] new-line
The clauses for the !$acc update directive are:
  host (list)
  device (list)
  if (condition)
  async [( scalar-integer-expression)]

## Slide 81: OpenACC Wait Directive
It causes the program to wait for completion of an asynchronous activity such as an accelerator parallel, kernel region or update directive
Specified by:
#pragma acc wait [(scalar-integer-expression)] new-line
  It will test and evaluate the integer expression for completion
  If no argument is specified, the host process will wait until all asynchronous activities have completed
  Can be specified per CPU/Thread basis.

## Slide 82: OpenACC runtime calls
int acc_get_num_devices( acc_device_t)
void acc_set_device_type(acc_device_t)
acc_device_t acc_get_device_type()
acc_set_device_num(int, acc_device_t)
int acc_get_device_num(acc_device_t)
int acc_async_test(int)
int acc_async_test_all()
void acc_async_wait(int)
void acc_async_wait_all()
void acc_init(acc_device_t)
void acc_shutdown (acc_device_t)
int acc_on_device(acc_device_t)
void* acc_malloc(size_t)
void acc_free( void*)

## Slide 83: Environment Variables
export ACC_DEVICE_TYPE=NVIDIA
export ACC_DEVUCE_NUM=1